## Slide 1: Introduction
Using a simple example with only two bidding zones, this presentation shows how spot prices and market flows are calculated.
Appendix 1 explains the procedure curtailment of spot bids.
In appendix 2, you’ll find a list of the terms and acronyms used in this presentation.
Concerning the documents referred to in this presentation:
  Unless otherwise stated, you can download the documents from www.houmollerconsulting.dk/facts-findings/.
This PowerPoint presentation is animated
  It’s strongly recommended to run the animation when viewing the presentation.
On most computers, you can start the animation by pressing F5.
  Now the presentation moves one step forward, when you press Page Down. It moves one step backward, when you press Page Up.

## Slide 2: Market coupling
Tomorrow’s plans for the cross-border
energy flows are calculated using the
purchase bids and sales offers sent by the
market players to the spot exchanges
This system is also called implicit auction
Market coupling is a day-ahead
grid congestion management system:

## Slide 3: Market coupling and spot price calculation – 1 For one hour. An exporting zone
€/MWh
MWh
Local sale
to exchange
Local purchase
from exchange
Price Plow
Exported
energy E
}
Price
without
mc
mc means
market coupling
The exchange’s local purchase
surplus is the exported energy E
Local demand
(sum of local
purchase bids)
Local supply
(sum of local
sales offers)
Without mc, the local price
is set at the intersection
between the local
demand curve and
the local supply curve.
This is the local
equilibrium price:
at this price, the local
sale to the exchange
is equal to the local
purchase from
the exchange
By setting Plow higher
than the local
equilibrium price,
the exchange gets a
local purchase surplus.

## Slide 4: Market coupling and spot price calculation – 2 For one hour. An importing zone
€/MWh
MWh
Price Phigh
}
Imported
energy E
Price
without mc
mc means
market coupling
Without mc, the local price
is set at the intersection
between the local
demand curve and
the local supply curve.
This is the local
equilibrium price:
at this price, the local
sale to the exchange
is equal to the local
purchase from
the exchange
Local demand
(sum of local
purchase bids)
Local supply
(sum of local
sales offers)
By setting Phigh lower
than the local
equilibrium price,
the exchange gets a
local sales surplus.
The exchange’s local sales
surplus is the imported energy E
Local sale
to exchange
Local purchase
from exchange

## Slide 5: Market coupling and spot price calculation – 3 For one hour. Only two bidding zones
Price Plow
Exporting zone
€/MWh
MWh
Exported
energy E
}
Importing zone
€/MWh
MWh
Price Phigh
}
Imported
energy E
Congestion revenue:
E * (Phigh – Plow)
}
E
Price
without
mc
Price without mc
mc means market coupling

## Slide 6: Setting an exchange price
To set a price, an exchange needs to have both purchase bids and sales offers.
This is true for any exchange – no matter what the exchange is trading.
However, a spot exchange can set a price in a bidding zone, even if the zone has sales offers only.
And a spot exchange can also set a price in a bidding zone, even if the zone has purchase bids only.
In such cases, setting a price is possible, if another zone has the opposite type of bids.
€

## Slide 7: Only sales offers in a bidding zone
Assume a bidding zone has sales offers only
  No purchase bids in the zone.
In this case, the zone becomes an exporting zone.
By means of buyers in other zones, a spot exchange can set a price in such a zone.

## Slide 8: Market coupling and spot price calculation – 4 For one hour. Only two bidding zones
Price Plow
Exporting zone
€/MWh
MWh
Exported
energy E
}
Importing zone
€/MWh
MWh
Price Phigh
}
Imported
energy E
Congestion revenue:
E * (Phigh – Plow)
}
E
Price without mc
mc means market coupling
No purchase bids in exporting zone

## Slide 9: Only purchase bids in a bidding zone
Assume a bidding zone has purchase bids only
  No sales offers in the zone.
In this case, the zone becomes an importing zone.
By means of sellers in other zones, a spot exchange can set a price in such a zone.

## Slide 10: Market coupling and spot price calculation – 5 For one hour. Only two bidding zones
Price Plow
Exporting zone
€/MWh
MWh
Importing zone
€/MWh
MWh
Price Phigh
Price
without
mc
mc means market coupling
No sales offers in importing zone
E
Congestion revenue:
E * (Phigh – Plow)
Imported
energy E
Exported
energy E

## Slide 11: Only two bidding zones Only one type of bid in each zone
Assume one zone has sales offers only.
And the other zone has purchase bids only.
If there’s ample cross-border grid capacity:
  In this case, the two zones will have the same spot price.
    The common price will be set by the intersection between the exporting zone’s supply curve and the importing zone’s demand curve.
  Hence, it will work as if we had one bidding zone only.
If the cross-border grid capacity is not big enough to allow a common price for the two zones:
  In this case, the prices are set as shown at the next slide.

## Slide 12: Market coupling and price calculation – 6 For one hour. Only two bidding zones
Price Plow
Exporting zone
€/MWh
MWh
Importing zone
€/MWh
MWh
Price Phigh
No purchase bids in exporting zone and no sales offers in importing zone
Exported
energy E
Congestion revenue:
E * (Phigh – Plow)
E
Imported
energy E

## Slide 13: Two bidding zones only No bids in one of the zones
Assume one of the two zones has neither purchase bids nor sales offers.
In this case, the two zones get the same spot price.
This common spot price is the price set in the zone having purchase bids and sales offers.
The other zone simply gets this price.
Price

## Slide 14: More than two bidding zones
The slides no. 5-8 in the PowerPoint presentation Energy island’s spot price and market coupling flows discuss a case, where you have several bidding zones
  With no purchase bids in one of the zones.
In the case, the bidding zone without purchase bids is supposed to be an energy island.
However, the case applies to any situation, where you have several bidding zones
  With one zone having sales offers only.
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone
Bidding
zone

## Slide 15: More information Spot price calculation without market coupling
It’s recommended to view the PowerPoint presentation Spot trading as a supplement to this presentation
  Appendix 1 of the presentation Spot trading shows how the spot price is calculated
    For a simple example, where you have one bidding zone only
      Consequently, no calculation of market coupling flows.

## Slide 16
Appendix 1
Curtailment of spot bids

## Slide 17: Curtailment of spot bids
This appendix explains the procedure applied if:
  A bidding zone has too few purchase bids.
  A bidding zone has too few sales offers.
For simplicity, at the following 4 slides, we’ll ignore market coupling
  Hence, we’ll consider an isolated bidding zone.

## Slide 18: Curtailment of spot sale offers – 1 Example for one bidding zone for one hour
€/MWh
MWh
1,000
800
Example: At min. price,
all the sellers in total
want to sell 1,000
MWh. However, even
at the min. price, all
the buyers in total will
only buy 800 MWh.
max.
price
Result: 1) The spot
price is the min. price.
Hence, only those
sellers, who will sell at
the min. price, get sale.
2) However, even each
of these sellers will
sell only 80% of the
amount offered at the
min. price!
Demand
Supply
min.
price

## Slide 19: Curtailment of spot sale offers – 2
This procedure is called ”curtailment of sales offers”.
  Only sellers willing to sell at the min. price, actually sell anything
    However, even each of these sellers will only sell a certain percentage of the volume offered at the min. price (as there are not buyers to the whole sale volume).
  All block sales offers containing the hour in question are rejected
    As a block bid is an all-or-nothing bid
      ie, either the seller sells the whole volume – or the seller sells nothing.

## Slide 20: Curtailment of spot purchase bids – 1 Example for one bidding zone for one hour
€/MWh
MWh
1,200
Example: At max. price,
all the buyers in total
want to buy 1,600
MWh. However, even
at the max. price, all
the sellers in total will
only sell 1,200 MWh.
max.
price
Result: 1) The spot
price is the max. price.
Hence, only those
buyers, who will buy at
the max. price, get
electricity.
2) However, even each
of these buyers will
get only 75% of the
amount wanted at the
max. price!
1,600
Demand
Supply
min.
price

## Slide 21: Curtailment of spot purchase bids – 2
This procedure is called ”curtailment of purchase bids”.
  Only buyers willing to buy at the max. price, actually get purchase
    However, even each of these buyers will only get a certain percentage of the volume wanted at the max. price (as there are not sellers to the whole purchase volume).
  All block purchase bids containing the hour in question are rejected
    As a block bid is an all-or-nothing bid
      ie, either the buyer buys the whole volume – or the buyer buys nothing.
”Curtailment of bids” is the common term for curtailment of sales offers and curtailment of purchase bids.

## Slide 22: Market coupling and curtailment of spot bids
With a bit of luck, market coupling can prevent curtailment of spot bids.
If a zone has too few purchase bids:
  Export of energy created by market coupling may remove the surplus of energy
    Thereby providing a spot price higher than the minimum price.
If a zone has too few sales offers:
  Import created by market coupling may eliminate the deficit of energy
    Thereby providing a spot price lower than the maximum price.
However, this is not always the case.
During the summer 2023, in large parts of Europe, we had hours with minimum spot prices.
In Western Denmark, some years ago, we had two hours where the spot price was at the maximum.

## Slide 23: Spot prices Sunday 2 July 2023 In €/MWh
Hour (CEST time) | Albania | HU | Croatia | Greece | AT | BE | DE-LU | FR | NL | UK | EE | LV | LT
00 - 01 | 95,25 | 16,45 | 16,45 | 111,75 | 16,45 | 16,45 | 16,45 | 16,45 | 16,45 | 29,10 | 16,45 | 16,45 | 16,45
01 - 02 | 87,17 | 3,17 | 3,17 | 107,92 | 3,17 | 3,17 | 3,17 | 3,17 | 3,17 | 18,66 | 3,17 | 3,17 | 3,17
02 - 03 | 85,55 | 0,01 | 0,01 | 105,69 | 0,01 | 0,01 | 0,01 | 0,01 | 0,01 | 2,44 | 0,01 | 0,01 | 0,01
03 - 04 | 85,02 | 0,00 | 0,00 | 101,39 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,01 | 0,00 | 0,00 | 0,00
04 - 05 | 83,24 | -0,01 | -0,01 | 100,49 | -0,02 | -0,03 | -0,03 | -0,03 | -0,03 | 0,01 | -0,03 | -0,03 | -0,03
05 - 06 | 80,36 | -0,05 | -0,05 | 104,55 | -0,05 | -0,05 | -0,05 | -0,05 | -0,05 | 0,00 | -0,05 | -0,05 | -0,05
06 - 07 | 78,59 | -0,02 | -0,02 | 168,35 | -0,03 | -0,05 | -0,05 | -0,05 | -0,06 | -0,01 | -0,02 | -0,02 | -0,02
07 - 08 | 81,24 | -0,15 | -0,18 | 120,31 | -0,29 | -0,49 | -0,50 | -0,47 | -0,51 | -2,90 | 0,00 | 0,00 | 0,00
08 - 09 | 67,35 | -0,95 | -1,11 | 20,12 | -1,75 | -2,90 | -2,95 | -2,75 | -2,97 | -10,06 | -0,10 | -0,10 | -0,10
09 - 10 | 55,71 | 0,00 | -0,71 | 0,00 | -6,42 | -13,70 | -15,07 | -12,92 | -16,90 | -13,82 | 0,01 | 0,01 | 0,01
10 - 11 | 48,61 | 0,55 | -3,91 | 3,00 | -11,08 | -23,07 | -37,00 | -23,01 | -60,00 | -16,10 | 0,01 | 0,01 | 0,01
11 - 12 | 37,38 | 0,99 | -7,38 | 0,01 | -23,54 | -6,46 | -98,11 | -19,17 | -252,92 | -6,48 | 0,00 | 0,00 | 0,00
12 - 13 | 39,49 | 0,05 | -12,35 | 0,20 | -38,68 | 0,00 | -167,96 | -23,78 | -449,57 | -4,49 | 0,00 | 0,00 | 0,00
13 - 14 | 36,06 | -34,00 | -45,76 | 0,00 | -86,93 | -17,00 | -266,92 | -20,00 | -500,00 | -14,23 | 0,00 | 0,00 | 0,00
14 - 15 | 31,26 | -500,00 | -500,00 | 0,00 | -500,00 | -100,00 | -500,00 | -55,66 | -500,00 | -41,95 | 0,00 | 0,00 | 0,00
15 - 16 | 35,33 | -32,88 | -64,34 | 0,00 | -134,94 | -120,00 | -399,00 | -134,94 | -500,00 | -47,53 | -0,08 | -0,08 | -0,08
16 - 17 | 48,04 | 2,59 | -12,65 | 49,89 | -36,61 | -100,00 | -124,21 | -79,44 | -172,39 | -30,37 | 0,00 | 0,00 | 0,00
17 - 18 | 69,42 | 37,96 | 32,63 | 80,00 | 0,08 | -32,74 | -35,18 | -27,38 | -35,18 | -0,01 | -0,03 | -0,03 | -0,03
18 - 19 | 95,26 | 50,83 | 47,77 | 101,69 | 19,18 | -3,86 | -6,01 | -0,01 | -6,01 | 3,07 | 0,00 | 0,00 | 0,00
19 - 20 | 117,19 | 86,24 | 80,93 | 109,30 | 40,76 | 7,94 | 4,83 | 13,37 | 4,88 | 30,81 | 4,97 | 4,97 | 4,97
20 - 21 | 134,2 | 89,24 | 87,27 | 110,75 | 77,30 | 69,80 | 69,09 | 71,04 | 69,10 | 72,15 | 28,47 | 28,47 | 28,47
21 - 22 | 127,25 | 90,06 | 89,37 | 112,47 | 86,72 | 85,70 | 85,61 | 85,91 | 85,58 | 85,68 | 28,28 | 28,28 | 28,28
22 - 23 | 114,75 | 94,90 | 94,90 | 102,62 | 94,90 | 94,90 | 94,90 | 94,90 | 94,90 | 90,66 | 21,33 | 21,33 | 21,33
23 - 00 | 104,19 | 86,08 | 86,08 | 123,84 | 86,08 | 86,08 | 86,08 | 86,08 | 86,08 | 81,47 | 16,83 | 16,83 | 16,83
Min | 31,26 | -500,00 | -500,00 | 0,00 | -500,00 | -120,00 | -500,00 | -134,94 | -500,00 | -47,53 | -0,10 | -0,10 | -0,10
Max | 134,20 | 94,90 | 94,90 | 168,35 | 94,90 | 94,90 | 94,90 | 94,90 | 94,90 | 90,66 | 28,47 | 28,47 | 28,47
Average | 76,58 | -0,37 | -4,58 | 72,26 | -17,32 | -2,35 | -53,87 | -1,20 | -89,02 | 9,42 | 4,97 | 4,97 | 4,97
 | Albania | HU | Croatia | Greece | AT | BE | DE-LU | FR | NL | UK | EE | LV | LT
This day had high production from both wind and solar
Sources: ALPEX, CROPEX, HUPX, HEnEx and Nord Pool

## Slide 24
Appendix 2
Terminology and acronyms

## Slide 25: Terminology and acronyms – 1 As used in this presentation
Bidding zone A geographical area, within which the players can trade electrical energy day-ahead without considering grid bottlenecks.
Block bid See appendix 1 of the PowerPoint presentation Market coupling – European price coupling.
Flow Short for market coupling flow.
Market coupling See the PDF document The Liberalized Electricity Market and the PowerPoint presentation Unbundling and EU’s Single Electricity Market.
Market coupling flow Plan for the next day’s cross-border energy flows calculated by the spot calculation system. See also market coupling.
Maximum price At the time of writing, for most spot exchanges in the SDAC area, the maximum price is 4,000 €/MWh.
Minimum price At the time of writing, for most spot exchanges in the SDAC area, the minimum price is -500 €/MWh.

## Slide 26: Terminology and acronyms – 2 As used in this presentation
SDAC Single Day-Ahead Coupling. See https://www.entsoe.eu/network_codes/cacm/implementation/sdac/
Spot calculation system In this document, this means the system, which calculates both the spot prices and the market coupling flows.
Spot exchange an exchange where players can do spot trading.
Spot price See the PowerPoint presentation Maximizing the economic value of market coupling and spot trading.
Spot trading In this document, this means trading electrical energy day-ahead with an exchange.
“Day-ahead” means the players are selling & buying electrical energy, which is produced & consumed the next day.
The prices, at which the players trade, are set by using the demand and supply curves created by the players’ bids.

## Slide 27: Thank you for your attention!
Anders Plejdrup Houmøller
Houmoller Consulting ApS
Tel. +45 28 11 23 00
anders@houmollerconsulting.dk
Web houmollerconsulting.dk